## Slide 1
⚡ LUBEGA
AI-POWERED ELECTRICITY THEFT DETECTION SYSTEM
Real-time CT bypass detection using Raspberry Pi + VotingClassifier ML
UEDCL Distribution Monitoring · Ndejje University Final Year Project
[Student Name 1] | [Student Name 2]
Supervisor: [Supervisor Name]
🟢 DASHBOARD LIVE — lubegacode.streamlit.app

## Slide 2
Introduction
The Problem — and Why It Matters
Uganda's Distribution Crisis
• 40-60% non-technical losses in Kampala urban areas (Bwaise, Kisenyi, Katwe)
• UGX 280 billion annual revenue lost by UEDCL
• 95% of meters have no real-time monitoring capability
• Manual detection: < 35% effective, 3-6 month delays
CT Bypass Tampering
The thief bypasses one or more Current Transformer (CT) clamps on the energy meter. Voltage registers correctly. Current is under-reported. Electricity is consumed but not fully billed. Result: 40-90% reduction in billed consumption — undetected for months.
Lubega — AI-Powered Electricity Theft Detection | Ndejje University
May 2026

## Slide 3
Project Objectives
1. Collect Labelled Data
Record ~160K readings across 8 CT bypass scenarios at 10-second intervals
2. Engineer 20 Features
Current/voltage imbalance, zero-value flags, power efficiency ratio
3. Train Ensemble ML Model
VotingClassifier (RF + XGBoost) — target AUC > 0.95
4. Deploy Edge Inference
Live inference on Raspberry Pi 4 as a systemd service
5. Build Cloud Dashboard
Real-time operator dashboard on Streamlit Community Cloud at $0/month
Lubega — AI-Powered Electricity Theft Detection | Ndejje University
May 2026

## Slide 4
Literature Review
What Exists — and the Gap
Nagi et al. (2011) IEEE Trans. Power Delivery
First demonstration of SVM-based NTL detection on smart meter data — established supervised classification as the dominant paradigm
Jokar et al. (2016) IEEE Trans. Smart Grid
Random Forests outperform SVMs on imbalanced NTL datasets — balanced class weights critical
Zanetti et al. (2017) IEEE Trans. Smart Grid
Ensemble methods (Voting, Stacking) consistently best single classifiers for fraud detection
Warden & Situnayake (2019) TinyML — O'Reilly
Edge ML on single-board computers is viable for real-time classification without cloud inference
Gap: No study addresses real-time 10-second edge inference for CT bypass detection in Uganda's distribution context.
Lubega — AI-Powered Electricity Theft Detection | Ndejje University
May 2026

## Slide 5
Methodology
System Architecture — 3 Layers
Layer 1 — Raspberry Pi 4 (Edge)
• CHINT DTSU666 meter via Modbus RTU RS485
• main.py: polls every 10s, aggregates every 15 min
• detect.py: reads latest_reading.json every 10s
• VotingClassifier inference locally on Pi
→
Layer 2 — Neon PostgreSQL (Cloud)
• lubega-production project (free tier)
• alerts table: pred, prob, phase readings, timestamp
• readings table: live meter values
• Pi writes via psycopg2 direct connection
→
Layer 3 — Streamlit Dashboard (LIVE)
• lubegacode-tbn4wlkpdrzqhjahqssdvf.streamlit.app
• KPIs: total alerts, 24h, latest prob, last alert
• Colour-coded alerts table (red >=90%, yellow >=70%)
• Live phase current/voltage/power charts
Lubega — AI-Powered Electricity Theft Detection | Ndejje University
May 2026

## Slide 6
ML Pipeline
Feature Engineering → Model → Inference
20 FEATURES = 9 Raw Meter Values + 11 Engineered
Raw (9)
• I_L1, I_L2, I_L3
• V_L1, V_L2, V_L3
• P_total
• PF_total
• Frequency
Engineered (11)
• I_imbalance, V_imbalance
• I_L1/L2/L3_zero flags
• V_L1/L2/L3_zero flags
• PF_zero flag
• I_total, P_per_I
Model
• VotingClassifier (soft)
• RandomForest 200 trees
• XGBoost 200 rounds
• AUC = 1.0000
• 14.4 MB on Pi
Deployment
• detect.py on Pi
• Reads JSON every 10s
• scaler.pkl → model.pkl
• prob > 0.5 → INSERT alert
• systemd auto-restart
Lubega — AI-Powered Electricity Theft Detection | Ndejje University
May 2026

## Slide 7
Results
Model Performance + System Deployment
1.0000
Test AUC (perfect classification)
160K
Training rows (8 bypass scenarios)
20
Feature dimensions per reading
< 1s
Inference latency on Raspberry Pi 4
✅ Dashboard Live — Confirmed
URL: lubegacode-tbn4wlkpdrzqhjahqssdvf.streamlit.app Status: Connected to Neon PostgreSQL lubega-production Displaying: KPIs (0 alerts — system monitoring), colour-coded table, phase charts, alert trend Next: Dennis deploys theft-detector.service on Pi → first real alert appears on dashboard
Lubega — AI-Powered Electricity Theft Detection | Ndejje University
May 2026

## Slide 8
Discussion
Achievements, Limitations, and What Comes Next
Achievements
✓ AUC 1.0 across all 8 bypass scenarios — model generalises to all CT bypass patterns encountered
✓ Zero recurring cloud cost — Neon + Streamlit free tiers sufficient for production monitoring
✓ Edge inference eliminates cloud round-trip — detection fires within 10 seconds of bypass
✓ Dashboard live and publicly accessible before Pi inference is deployed
✓ Structurizr C4 architecture + 4 ADRs document all design decisions
✓ AUC 1.0 across all 8 bypass scenarios
✓ $0/month cloud infrastructure
✓ 10-second detection latency (edge inference)
✓ Dashboard live before Pi inference deployed
✓ Structurizr C4 architecture + 4 ADRs documented
Limitations & Next Steps
→ Model trained on 1 meter only — test on multiple meters with varied loads
→ CT bypass scenarios only — illegal connections and meter clocking not covered
→ theft-detector.service not yet deployed on Pi — end-to-end test pending
→ No SMS/WhatsApp alerting yet — Africa's Talking API planned
→ ONNX export for faster Pi inference — future optimisation
Lubega — AI-Powered Electricity Theft Detection | Ndejje University
May 2026

## Slide 9
Conclusion & Recommendations
Lubega demonstrates that high-accuracy, real-time electricity theft detection is achievable at zero cloud cost using commodity hardware and open-source ML.
The VotingClassifier (RF + XGBoost) achieves AUC = 1.0000 on 8 CT bypass scenarios. The Streamlit dashboard is live. The Pi inference service is the remaining critical step to full system operation.
Recommendations:
1. Deploy theft-detector.service on Pi — completes end-to-end pipeline
2. Add Africa's Talking SMS alerts — immediate operator notification
3. Extend to multiple meters via ZeroTier network — scale to district level
4. Publish as open-source reference architecture for African utility NTL detection
Lubega — AI-Powered Electricity Theft Detection | Ndejje University
May 2026

## Slide 10
References
UEDCL Annual Report 2023. Uganda Electricity Distribution Company Limited, Kampala.
World Bank (2020). Electricity Distribution Losses in Sub-Saharan Africa. World Bank Group.
Nagi, J. et al. (2011). Nontechnical loss detection using support vector machines. IEEE Trans. Power Delivery, 25(2).
Jokar, P. et al. (2016). Electricity theft detection in AMI using customers' consumption patterns. IEEE Trans. Smart Grid, 7(1).
Zanetti, M. et al. (2017). A tunable fraud detection system for AMI using short-lived patterns. IEEE Trans. Smart Grid, 10(1).
Warden, P., & Situnayake, D. (2019). TinyML: Machine Learning with TensorFlow Lite. O'Reilly Media.
CHINT Electric (2022). DTSU666 Modbus Communication Protocol Specification. CHINT Group Co., Ltd.
Lubega — AI-Powered Electricity Theft Detection | Ndejje University
May 2026